## Slide 1: Update: Data analyses Tracking-Task A and B
14.09.2022

## Slide 2: Preprocessing
FPz as reference electrode
Downsampling to 250 Hz
Highpass filter for 1 Hz
Remove line noise at 50 Hz
Remove bad channels (flat, minimum channel correlation)
Lowpass filter 40 Hz
Interpolate bad channels
Rereference to average
Merge data for task A & B: for ICA, epoch data, detrending, artifact rejection
  run ICA (extended infomax algorithm)
  Iclabel: keep only those Ics that are labelled as neural component with at least 0.5 probability
  Visual checks of remaining components
Parallelize behavioral and EEG data  add triggers etc.
Epoch data: 1) for whole trial (-1 13)  baseline correction for fixcross interval (-750 0)
  2) -1 4 for task A and B, later reduced to relevant time interval
Artifact rejection for segments

## Slide 3: Wavelet analysis
Morlet wavelet, 5 cycles, length of wavelet kernel = 3
Frequencies: 1-35 Hz (although hp-filter for 1 Hz was applied before)
Conditions:
  Task A: trajectory segments  random1, constant, random2
  Task B: occlusion segments  occluded, non-occluded/visible

## Slide 4: CBPT A & B
Monte-Carlo, 1000 iterations
Alpha = 0.001, cluster alpha = 0.001
For alpha (8-12 Hz), theta (4-7 Hz) and beta band (13-30 Hz)
Task A: averaged only in frequency dimension
Task B: averaged in both time and frequency dimension

## Slide 5: Pipeline DICS Beamforming

## Slide 6: Task A: alpha power
Significant time interval: 0 – 512 ms
Significant time interval: 0 – 512 ms

## Slide 7: Task A: beta power
Significant time interval: 0 – 432 ms
Significant time interval: 0 – 420 ms

## Slide 8: Task A: theta power
Significant time interval: 0 – 1.96 s
Significant time interval: 0.1 – 0.8 s

## Slide 9: Task B: theta power
Beamforming performed for whole time window: 0-2 s